## Slide 1: Energy Oriented Business Administration Prof. Dr. Johannes Kals 6 Organization and ISO 50001 Energy Management Systems
Content
What are ISO Standards?
ISO 50000-Series Energy Management Systems
Integrated Management

## Slide 2
Independent, non-governmental international organization
Participation of industry, retail, science, consumers, agencies and government
Development of standards in fixed procedures striving for consensus
More than 20,000 standards (mechanical engineering, chemical technology, electronics …).
The International Organization for Standardization (ISO) issues a large number of mostly technical standards with a global reach

## Slide 3
CEN (Comité Européen de Normalisation); European Committee for Standardization)
International Organization for Standardization (ISO)
ISO unifies more than 160 national bodies
(here example Germany with an intermediate Europe)
German Institute for Standardization

## Slide 4
Environmental Management (first issued 1996, ISO 14000 series)
Energy Management Systems (EnMS, 2011, 50000 series)
Greenhouse Gases including Carbon Dioxide (in process, 14060 series)
Quality Management (QM, first issued 1987, ISO 9000 series)
In the 1980s, the idea of technical standardization was enlarged to management systems:

## Slide 5
How does it work? ISO prescribes which elements an organization has to implement, e.g,
  procedures to measure the quality of products (ISO 9000),
  indicators to alert if environmental regulation could be violated (ISO 14000),
  or targets to improve energy performance (ISO 50000).
To say simplifying: as standards contains a checklist what an organization has to put into practice in the respective field.

## Slide 6
To confirm that all elements of the respective
ISO management standard
are implemented adequately,
a third-party company conducts an audit and grants a certificate.
Thus, stakeholders of the organization may be sure that the requirements of the management system are met.
Those certifying/ auditing companies have to be accredited
(see next chart).

## Slide 7
Institutions of certification
Company heading for a certification of management system in quality, environment, energy etc.
Consulting company as optional support, it has to be separated from the certifier
National accreditation authority
Certifying/ auditing company
Consulting
cooperation possible
Accreditation
Audit and certification
Source: Kals, ISO 50001, 2015, p. 8.
Notes: Source: Kals, Johannes: ISO 50001 Energy Management Systems – What managers need to know about energy and
business administration, New York 2015, P. 8.
Figure: 1.1: Institutions of certification
Certification as EnMS as parties:
First party: Company itself
Second party: Stakeholder
Third party: Auditor
Fourth party: Public authority
Some organizations or companies decide to undergo certification in order to improve its management system. In doing so, they should present their
achievement to stakeholders and investors. Here comes the role of the auditor to verify that all requirements are met and grant a certificate.

## Slide 8
Sorting the different parties:
The accrediting agency may be seen as fourth-party
Second-party – a stakeholder, namely audits of customers
First-party – our focus company, internal audit
Third-party certification – independent, accredited certifier

## Slide 9
Plan
Do
Check
Act
Management standards rely on the the PDCA-cycle,
guaranteeing for a continual improvement process –
internal and external audits have to be repeated regularly

## Slide 10
Content
What are ISO Standards?
ISO 50000-Series Energy Management Systems
Integrated Management

## Slide 11
Where is further information?
Which are the detailed requirements?
Standards are costly, on iso.org the table of contents may be viewed.
The next charts present a cross-reference table linking the ISO 50001-chapters Energy Management System to business function.

## Slide 12
ToC of ISO 50001 | Energy oriented business administration: business functions
4 Energy management system requirements 4.1 General requirements 4.2 Management responsibility 4.2.1 Top management 4.2.2 Management representative | Structural organization of energy management
4.3 Energy Policy | Relationship between energy policy and strategic planning, business ethics, and Corporate Social Responsibility
4.4 Energy planning 4.4.1 General 4.4.2 Legal requirements and other requirements | Compliance management helps to fulfill all external, internal legal, and other requirements
4.4.3 Energy review | Linking energy reviews or balances to accountancy: cost-type accounting (smart metering, factory data capture, internet of things) cost-center accounting (energy flow and sankey diagrams) cost object accounting (life-cycle assessment)
4.4.4 Energy baseline 4.4.5 Energy Performance Indicators (EnPIs) | Managerial accounting, for example EnPIs and energy oriented balanced scorecard
Overview of ISO 50001, linking the table of content to business functions, taken from
Kals, Johannes: ISO 50001 Energy Management Systems – What Managers Need to Know About Energy and Business Administration, Business Expert Press, New York, NY, 2015.

## Slide 13
4.4.6 Energy objectives, energy targets, and energy management action plans | Investment appraisal: Identifying profitable investments with methods as Total Cost of Ownership, optimal replacement point, sensitivity analysis, energetic amortization
4.5 Implementation and operation 4.5.1 General 4.5.2 Competence, training, and awareness | Human Resource Management: Communicating EnMS inside the organization
4.5.3 Communication | Marketing and Customer Relationship Management: Taking into account the informed customer using sustainability apps and Big Data
4.5.4 Documentation | Quality Management: Documentation of integrated management systems explaining the ways and perspectives of integration
4.5.5 Operational control | Maintenance: Smart metering, management cockpits, mobile computing
4.5.6 Design 4.5.7 Procurement of energy services, products, equipment, and energy | Energy in further corporate functions Procurement of energy Finance and contracting to procure energy Procurement other than energy Logistics Facility Management Production planning and production Green IT
4.6 Checking 4.6.1 Monitoring, measurement, and analysis 4.6.2 Evaluation of compliance with legal requirements and other requirements 4.6.3 Internal audit of the EnMS 4.6.4 Nonconformities, correction, corrective action, and preventive action 4.6.5 Control of records | Control and audits
4.7 Management review | Internal revision

## Slide 14
Drilling down one layer deeper:
Next chart as example of the implementation of
Energy objectives, energy targets, and energy management action plans

## Slide 15
Action | Department–person responsible | Target date | Target of energy conservation/year and carbon conservation/year | Budget, cost reduction/year, return on investment (ROI) pay-back (optional: carbon amortization)
Replace air compressor | Facility Management, technical services—Enid Energy | June 30th, next year | 20,000 kWh/year 10,000 kg CO2/year | $24,000 budget $8,000 per year savings 33% ROI 3 years pay-back
Implement carbon accounting | Accountancy—Carl Carbon | March 31th, next year | Pilot project based on spreadsheet paralleling established cost accounting gate-to-gate involving a student | $4,000 cost savings, ROI, and pay-back hard to measure
Replace five old trucks | Logistics—Clint Climate | End of the year | $3,750 dollar per year fuel cost cut 6,500 kg CO2/year | Profitability has to be assessed involving reduced maintenance cost, better reliability, new technical features of trucks, and so forth.
Training good housekeeping | Energy management representative and human resources—Ephron Efficient and Consuela Conservation | June 30th next year | Rule of thumb: 20% overall conservation by changes in behavior. Conservation depending on company size | Zero (variable) cost, cost-reduction see following box ROI theoretically infinite pay-back immediate
… |  |  |  | 

## Slide 16
Pros | Cons
A certification incentivizes a company to completely understand and exploit potential of energy savings and cost reductions. Further, non energy-related improvements of management could radiate from this project. A whole bundle of nontangible effects will be attained by sending a highly visible signal to stakeholders. The effort can be very small if quality and environment are already certified and followed by an integrated approach. In some countries, branches like the automotive, pharma, or food have reached a saturation of almost a 100% concerning quality certification. Lacking certification, companies can hardly enter the market, not even as suppliers. | Certifications cause internal costs during preparation of the system; external costs arise through consulting and auditing. The seemingly endless inclination of ISO to issue new standards. Overregulation may hinder a smooth workflow and exaggerate documentation needs. Once a certificate is attained, stakeholders will be sensitive to uphold it. Thus, companies may feel compelled to conduct a re-audit after three years, with the obligation to follow further requirements that could be issued.
Should a company go for a certificate?

## Slide 17
An example of practical benefits
An example showing the importance of process-orientation and co-operation between departments: Compressed air is produced by the energy or facility management department of a company and led by hundreds of pipelines into the workshops. If a leak of 0.5 centimeters in some hidden basement fails to be discovered, 30 liters of compressed air will be lost per second, representing 27,000 kilowatt-hours of energy and several thousand dollars in costs per year (depending on the local price).
What´s the role of ISO 50001?
ISO requires businesses to look at this process of energy supply holistically. Therefore, they must plan, conduct, and document regular leakage checks.
Costs and benefits of management systems are often scattered throughout the energy supply process. It’s important to establish consumption, distribution, and possible leakages by measuring consumption and assigning usages to cost-centers. This provides an incentive for efficient-energy use, e.g., by reducing the pressure, switching the system off at night. …
The established management rules have to be considered as a starting point of improvement.

## Slide 18
Content
What are ISO Standards?
ISO 50000-Series Energy Management Systems
Integrated Management

## Slide 19
Physical or administrative process
Quality
Environ-ment, eco-efficiency
Energy, carbon
Accounting Cost
CSR
Further perspec-tives
What means integrated management?

## Slide 20
Integration through …
Documentation and data integration
(structural)
Organization
Three pillars of sustainability
: „… beating companies to competitiveness!“

## Slide 21: Importance and hierarchy of documentation
Handbook, adressed to everyone including top management
Procedures, description of cross-functional workflows
Job instruction for one workplace or activity
Records, formulars, automized data logging and tracability of daily business
Further applicable documents
Combining with presentations about digitalization, Internet of Things, In-Memory Databases and further technical options of data integration
Notes: Source: Kals, Johannes: ISO 50001 Energy Management Systems – What managers need to know about energy and
business administration, New York 2015, P.169.
Figure 18.1: Hierarchy of documentation.

## Slide 22: Integration through (structural) organization – energy manager as part of an integrated advisory staff
Top management
Advisory staff managers: Quality, environment, energy, safety …
Procurement
Operations
Sales
Source: Kals, ISO 50001, 2015, p. 87
Notes: Source: Kals, Johannes: ISO 50001 Energy Management Systems – What managers need to know about energy and
business administration, New York 2015, P. 87.
Figure 10.1: Energy manager as advisory staff.
The figure illustrates the first option of an energy manager holding an advisory function in a staff department.

## Slide 23
Integrated (sustainability) management, balances, reporting, and disclosure means to describe the taking and giving between companies and their economic, natural, and social environment:
Profit
Planet
People
Economic balance sheet:
International Financial Reporting Standards (IFRS), U.S.
Generally Accepted Accounting Principles (US-GAAP), national legislation, etc. Monthly, quarterly, yearly, etc.
Internal, external, tax related, etc.
Environmental balance sheet:
waste and recycling, water, emissions, energy.
Energy balance condensed out of environmental balance
Social balance sheet, indicators measuring
diversity nondiscrimination donations
fair wages
developing countries
compliance
etc.
Carbon balance by evaluating energy use and emissions
Thinking sustainability holistically while implementing ISO standards or improving operations with other methods (chart as repetition from „balances“ presentation)
Source: Kals, ISO 50001, 2015, P. 16.
Notes: Source: Kals, Johannes: ISO 50001 Energy Management Systems – What managers need to know about energy and
business administration, New York 2015, P. 16.
Figure 2.1: Integrated sustainability management and balance sheet.
Types of balances to integrate EnMS to sustainability Management.
Sustainability means development that meet the needs of present without compromising the future generation ability to meet their own needs.
Sustainability look at three main aspects: Economic aspect, Environmental aspect, and social aspect.
23

## Slide 24
Implementing energy management and other ISO standards as project of organizational development/ change management:
Participation of process „stakeholders“
Talking about „losers“ and creating perspectives for them
Striving for integration with the upcoming options of digitalization

## Slide 25
Exercise
Elaborate some typical rules, regulations, or procedures which have to be establishes in order to meet the requirements of
ISO 9001
ISO 14001
ISO 50001
Think of a company in producing industry, or just a the firm you know best.
Did you got already in contact with certified management systems in the companies you had insight (internship, apprenticeship, …)?